## Slide 1
Computer Instructions are broadly classified into 3 different categories:
Data Transfer Instruction
Data Manipulation Instruction
Program Control Instruction
Data Transfer Instructions
Data transfer instructions transfer the data between memory and processor registers, processor registers, and I/O devices, and from one processor register to another. There are eight commonly used data transfer instructions. Each instruction is represented by a mnemonic symbol.
The table shows the eight data transfer instructions and their respective mnemonic symbols.
Name | Mnemonic Symbols
Load | LD
Store | ST
Move | MOV
Exchange | XCH
Input | In
Output | OUT
Push | PUSH
Pop | POP

## Slide 2
The instructions can be described as follows −
Load − The load instruction is used to transfer data from the memory to a processor register, which is usually an accumulator.
Store − The store instruction transfers data from processor registers to memory.
Move − The move instruction transfers data from processor register to memory or memory to processor register or between processor registers itself.
Exchange − The exchange instruction swaps information either between two registers or between a register and a memory word.
Input − The input instruction transfers data between the processor register and the input terminal.
Output − The output instruction transfers data between the processor register and the output terminal.
Push and Pop − The push and pop instructions transfer data between a processor register and memory stack.

## Slide 3
Data Manipulation Instructions
Data manipulation instructions have computational capabilities. They perform arithmetic, logic, and shift operations on data.
There are three types of data manipulation instructions are as follows −
Arithmetic Instructions
Arithmetic operations include addition, subtraction, multiplication, and division. Some computers provide instructions only for addition and subtraction operations and generate multiplication and division operations from these two operations. Each instruction is represented by a mnemonic symbol.
The table shows some of the arithmetic instructions and their respective mnemonic symbols.
Name | Mnemonic
Increment | INC
Decrement | DEC
Add | ADD
Subtract | SUB
Multiply | MUL
Divide | DIV
Add with carry | ADDC
Subtract with borrow | SUBB
Negate(2’s complement) | NEG

## Slide 4
Name | Mnemonics
Clear | CLR
Complement | COM
AND | AND
OR | OR
Exclusive-OR | XOR
Clear carry | CLRC
Set carry | SETC
Complement carry | COMC
Enable interrupt | EI
Disable interrupt | DI
Logical and Bit Manipulation Instructions
Logical instructions carry out binary operations on the bits stored in the registers. In logical operations, each bit of the operand is treated as a Boolean variable. Logical instructions can change bit value, clear a group of bits, or can even insert new bit value into operands that are stored in registers or memory words. Each logical instruction is represented by mnemonic symbols.

## Slide 5
Shift Instructions
Shift instruction helps to shift the bits of an operand to the right or the left. The direction of the shift is based on specific instructions. The operand is first loaded into the accumulator and then the shift operation is performed bit by bit.

## Slide 6
Program Control Instructions
Instructions of the computer are always stored in consecutive memory locations. These instructions are fetched from successive memory locations for processing and executing.
When an instruction is fetched from the memory, the program counter is incremented by 1 so that it points to the address of the next consecutive instruction in the memory. Once a data transfer and data manipulation instruction are executed, the program control along with the program counter, which holds the address of the next instruction to be fetched, is returned to the fetch cycle.
Data transfer and manipulation instructions specify the conditions for data processing operations, whereas the program control instructions specify the conditions that can alter the content of the program counter.
The change in the content of the program counter can cause an interrupt/break in the instruction execution. However, the program control instructions control the flow of program execution and are capable of branching to different program segments.
Some of the program control instructions are listed in the table.
Name | Mnemonics
Branch | BR
Jump | JMP
Skip | SKP
Call | Call
Return | RET
Compare (by Subtraction) | CMP
Test (by ANDing) | TST